## Slide 1: Scale Up
Alireza Ghassempour
Professor of Analytical Chemistry
Medicinal Plants and Drugs Research Institute
Shahid Beheshti University
Sept 2020

## Slide 2: THEORETICAL CONSIDERATIONS IN SCALE-UP
In order to have a successful scale-up it is desirable to maintain kinetic (particle size, pore size, ligand chemistry, temperature and mobile phase) and dynamic (bed height, flow velocity and packing density) equivalence between the chromatography columns used in the laboratory and the pilot plant. This objective can be accomplished by using identical stationary and mobile phases in the two columns and operating them at identical bed height, linear flow velocity, protein loading (mg protein per mL of resin), feed conditions, gradient length, and gradient slope. The most common procedure used to increase column volume is to increase the column diameter so that the column volume increases proportion at el.

## Slide 3
20
Purification of Picrocrocin
C18-30 µm-250*4.6mm
Loading:3mg
Flow rate:0.5 ml/min
C18-30 µm-500*100mm
Loading:3gr
Flow rate:236 ml/min
C18-30 µm-300*19mm
Loading:60mg
Flow rate:8 ml/min
Scale up
Scale up
Scale up
Notes: بدین صورت که ابتدا شرایط جداسازی در مقیاس تجزیه ای با ستونی که مشاهده میکنید بهینه شد سپس برای scale up کردن وخالص سازی با ستون تهیه ای احتیاج به یک گام میانی یا به اصطلاح یک ستون حد واسط بود که ستونی با ابعاد 300*19 طراحی ساخته و داخل پژوهشکده پر شد پس از تایید مراحل scale up از ستون هدف در مقیاس نیمه صنعتی استفاده شد

## Slide 5
Physical Overview

## Slide 6
Column efﬁciency as a function of particle size and type. Sample, naphthalene.
Conditions: 50 × 4.6-mm, C18 columns; mobile phase is 60%acetonitrile-watermobile phase; 23◦C.

## Slide 7
A typical scale-up from laboratory to pilot plant is on the order of 50–100-fold. This is frequently followed by a 10–50-fold scale-up from pilot plant to final commercial manufacturing scale.
The usual approach is to hold the plate count constant upon scale-up and increase the feed volume and column volume proportionately. This approach was originally based on the assumption of linear adsorption.
Simple Scale-Up Calculation

## Slide 10
Waters company program

## Slide 11
Agilent co.

## Slide 12
System dwell volume determination for preparative systems.

## Slide 13
The process of developing a focused gradient stats with an analytical focusing run using a linear gradient profile from 2 to 98% organic solvent. The analytical scouting run gives us the retention time of the target compound. The exact gradient conditions at elution of the individual target compound are calculated from the result of scouting run when dwell volume and column dead volume of the system have been determined beforehand.
The offset time between the programmed solvent and the actual solvent composition at the column head is calculated by dividing combined void volume by the flow rate. The virtual elution point, which reflects the actual solvent composition when the peak has been detected is calculated by determination of the gradient composition after subtracting the offset time from the retention time.

## Slide 14
Agilent co.

## Slide 16
Focused gradient profiles for target compounds with different polarities.
The dashed line represents an alternative step-gradient profile.
Agilent co.

## Slide 17: Recycling Development

## Slide 19
S. Mollayi, et al, Acta Chromatographia, 27 (2015) 387-398.

## Slide 20: LC × LC

## Slide 21: Multi-modal and mixed-bed separations are often confused.
2D LC or LC×LC method which either combination of two columns with different stationary phases or by use of two columns with the same stationary phase running under different mobile phases.
Mixed-bed stationary phases where a mixture of two stationary phases are packed into a single column (or columns are coupled), or where the stationary phase shows multiple retention mechanisms.

## Slide 22
Column combinations in LCxLC systems (up to May 2014)

## Slide 24
Paclitaxel structure
A. Ghassempour, et al., Journal of Liquid Chromatography & Related Technology, 31(2008) 382-394.
A. Ghassempour, et al., Journal of Liquid Chromatography & Related Technologies, 32, (2009) 1434-1447.
10-Deacetylbaccatin III structure

## Slide 25: HPLC calculator: software for chromatographic performance evaluation and HPLC method transfer
https://ispso.unige.ch/labs/fanal/hplc_calculator:en

## Slide 26: Analytical Optimization

## Slide 27
Total extract
Total crocins
Crocin I
Picrocrocin
Preparative isolation optimization

## Slide 28
Thalidomide was widely marketed in over 46 countries as a sleep aid. Its use during pregnancy was responsible for over 10,000 children born with profound birth defects. Thalidomide would have been approved in the United States were it not for the vigilance of a medical officer, Frances O. Kelsey.
The public health catastrophe prompted stronger regulation (Kefauver–Harris Amendment of 1962) for demonstrating the safety of a product prior to marketing. Although it was commonly thought the toxicity resided solely with the S(−) form of thalidomide, several in vitro studies showed that the drug could racemize quickly in various aqueous media. Metabolic inversion has been observed with other compounds, such as 2-arylpropionic acid (2-APA) and mandelic acid.

## Slide 29
Mandelic acid
Synthesis of vancomycin chiral stationary phase

## Slide 30
The docking result of mandelic acid with vancomycin. (A) Different available binding sites for R and (B) S mandelic acid
enantiomers. (C, D) The representative R and S ligands were compared. The molecular surface of vancomycin is colored by element

## Slide 31
Circular dichroism (CD) spectra of vancomycin with mandelic acid enantiomers, (S)-(+)-mandelic acid (S-MA), (R)-(−)-mandelic acid (R-MA), and vancomycin (vanco)
M. Shahnani, et al, Chirality 2020, DOI: 10.1002/chir.23273

## Slide 32
Three Scale Up Methods:
Stack Injection
Counter Current Chromatography
Simulated Moving Bed Chromatography (SMB)

## Slide 33
Chromatograms of 1000 ppm (up) and 3000 ppm (down) of propranolol in F = 1 mL min−1 and MP composition of 40% 2‐propanol, 0.6% DEA, related to minimizing RT in Rs ≥ 1.7 (sample solvent was identical to the MP)
Chromatograms for 3000 ppm of propranolol in stacked injection mode (F = 1 mL min−1 and MP composition was 40% 2‐propanol, 0.6% DEA in n‐hexane; sample solvent was identical to the MP)
Overloaded chromatogram for 20,000 ppm of propranolol in F= 1 mL min−1 and MP composition of 10% ethanol
and 0.60% DEA in n‐hexane, related to maximizing Rs (sample solvent was identical to the MP)
M. Taheri, et al., Chirality 29 (10) (2017) 579-588.

## Slide 34
Basic Principle
Mobile Phase
Feed
Continuous Countercurrent Chromatography
stationary column
A sample is injected in the centre of a stationary column
The two components move at different speeds and are separated
If we now move the column from right to left, at a speed halfway
between that of the solutes, they now move in different directions ...

## Slide 35
Basic Principle
Mobile Phase
Feed
column
The two solutes now move in different directions relative to a stationary
observer. If the column is very long, the bands will continue to separate.
Continuous Countercurrent Chromatography

## Slide 36
Basic Principle
Mobile Phase
Feed
column
If we continue to add sample at the center, the components will continue
to separate
Continuous Countercurrent Chromatography

## Slide 37
Simulated Moving Bed Chromatography (SMB)

## Slide 39
Thank you for your attention